## Slide 1
18 Jan 2023
© 2022 California Institute of Technology. Government sponsorship acknowledged.
NASA’s Multi-Angle Imager for Aerosols (MAIA) Investigation in Africa: An Integrated Satellite and Surface Monitoring Approach for Mapping Speciated Particulate Matter Air Pollution
Sina Hasheminassab,1 David J. Diner,1 Araya Asfaw,2 Jeffrey Blair,3
Rebecca Garland,4 Christina Isaxon,5 Juanette John,6 Kristy Langerman,7 Yang Liu,8 Christian L’Orange,9
Tesfaye Mamo,2 Randall V. Martin,10 Lotta Mayana,11 Mogesh Naidoo,6 Christopher Oxford10
1Jet Propulsion Laboratory, California Institute of Technology, Pasadena, CA; 2Addis Ababa University, Addis Ababa, Ethiopia; 3AethLabs, San Francisco, CA; 4University of Pretoria, Pretoria, South Africa; 5Lund University, Lund, Sweden; 6Council for Scientific and Industrial Research, Pretoria, South Africa; 7University of Johannesburg, Johannesburg, South Africa; 8Emory University, Atlanta, GA; 9Colorado State University, Fort Collins, CO; 10Washington University, St. Louis, MO; 11NerdyChemists Forensic and Industrial Science, Pretoria, South Africa

## Slide 2: MAIA Earth Venture Instrument Investigation
MAIA was selected in 2016 as a NASA Earth Venture Instrument (EVI) investigation with a primary emphasis on societal benefit.
MAIA’s EVI objective is to link exposure to different PM types (mixtures of particles having different sizes, shapes, and compositions) with human health.
MAIA applies and extends current satellite-based methodologies to enable mapping of speciated PM in selected metropolitan areas around the world.
NASA and the Italian Space Agency (ASI) are partnering on the MAIA mission, with ASI contributing the host spacecraft, launch, and complementary science.
Satellite launch: ~2024
Baseline flight mission duration: 3 years

## Slide 3: Key Elements of the MAIA-EVI Investigation
Satellite instrument | Surface monitor network | Chemical transport model | Health records
Privacy protected
Epidemiological
studies
Public products
Birth, death, and hospitalization data
Daily concentration maps of PM10, PM2.5, speciated PM2.5 at 1-km spatial resolution
Completed in October 2022
(
)

## Slide 4: Current MAIA-EVI Target Areas
Primary Target Areas (PTAs) are chosen by the MAIA Science Team for conducting and supporting the MAIA health studies
Secondary Target Areas (STAs) are areas of interest (e.g., cities with major pollution, aerosol source regions, climatically important cloud regimes), but where health studies are not mandated
MAIA Investigation is Target Based
Target area dimensions: 360 km x 480 km

## Slide 5: Current MAIA Target Areas in Africa
Primary Target Areas (PTAs) are chosen by the MAIA Science Team for conducting and supporting the MAIA health studies
Secondary Target Areas (STAs) are areas of interest (e.g., cities with major pollution, aerosol source regions, climatically important cloud regimes), but where health studies are not mandated

## Slide 6: Current Plans for Health Studies in African PTAs
PTA | Health outcomes/exposure timescale | Source/geocoding | MAIA lead | Local investigator
ETH-AddisAbaba | Preeclampsia, low birth weight and tuberculosis, child mortality/growth/lung function/cognition (Addis Ababa) | Birth cohort through Lund University and Armauer Hansen Research Institute | M. Jerrett B. Ritz | E. Malmqvist (Lund University)
 | Respiratory morbidity, lung function, cognition (Adama) | Young children cohort through Lund University |  | 
ZAF-Johannesburg | Cause-specific mortality due to ischemic heart disease, stroke, pneumonia, COPD, diabetes | Statistics South Africa | M. Brauer | J. Wichmann (Univ. of Pretoria)
Acute | Subchronic | Chronic
Address | Postal code | Municipality

## Slide 7: Surface PM Monitoring
 | Existing monitoring networks |  | SS5-PM2.5 filter-based sampler | Aerosol Mass and Optical Depth (AMOD) | microAeth MA350 aethalometer | PA-II-SD
Vendor | Various vendors |  | AirPhoton (SPARTAN network) | Colorado State University | AethLabs | PurpleAir
Pollutants | PM2.5 speciation, total PM2.5, total PM10 |  | PM2.5 speciation | PM2.5 speciation | Black carbon | Total PM2.5
Target areas | All target areas |  | CHN-Beijing (x1) | CHN-Beijing (x1) | CHN-Beijing (x1) | ETH-AddisAbaba (x10)
 |  |  | ETH-AddisAbaba (x1) | ETH-AddisAbaba (x2) | ETH-AddisAbaba (x2) | 
 |  |  | IND-Delhi (x1) | IND-Delhi (x3) | IND-Delhi (x1) | 
 |  |  | ISR-TelAviv (x2) | TWN-Taipei (x2) | USA-Los Angeles (x1) | 
 |  |  | TWN-Taipei (x2) | USA-Atlanta (x1) |  | 
 |  |  | USA-Los Angeles (x1) | USA-Los Angeles (x1) |  | 
 |  |  | ZAF-Johannesburg (x2) | ZAF-Johannesburg (x1) |  | 
MAIA project is deploying additional surface PM monitors in selected target areas to augment existing monitoring networks
Where available, MAIA project collects data from existing ground-based PM monitoring networks
Regression of retrieved aerosol properties against surface monitor (total and speciated PM) data is used to calibrate the aerosol-to-PM transformations
Although launch of the satellite instrument is not expected until 2024, surface PM measurements are being collected prior to launch to establish baseline pollution levels and exercise MAIA’s ground data processing software.

## Slide 8
Surface PM Monitoring Sites in Ethiopia PTA

## Slide 9
Addis Ababa University
Alert Hospital
Black Lion Hospital
PurpleAir PA-II-SD
Surface PM Monitoring Sites in Ethiopia PTA
UN Economic Commission for Africa
Environmental Protection & Green Development Commission
Note: These photos are examples of the operational sites; they do not depict all monitoring sites.

## Slide 10
AirPhoton SS5 PM2.5 Sampler
(SPARTAN Network)
CIMEL Sun Photometer
(AERONET Network)
US Embassy Warehouse (Jacros)
US Embassy Warehouse (Jacros)
Surface PM Monitoring Sites in Ethiopia PTA

## Slide 11
Monthly Average PM2.5 Measured by PA Sensors Across Addis Ababa
Average PM2.5 Measured by PA Sensors Across Addis Ababa
PM2.5 levels show strong spatial and temporal variations in Addis Ababa
Preliminary Surface PM Monitoring Results in Ethiopia PTA

## Slide 12
Preliminary Surface PM Monitoring Results in Ethiopia PTA
Average PM2.5 levels in Delhi, Beijing, and Addis Ababa are comparable, but substantially higher (>2x) than in Pasadena.
Average black carbon concentrations vary from less than 1 µg/m3 in Pasadena to over 8 µg/m3 in Addis Ababa (US Embassy, Jacros).
Black carbon makes up, on average, 6% of PM2.5 mass in Pasadena and Beijing, 10% in New Delhi and Addis Ababa (US embassy, Central), and over 25% in Addis Ababa (US Embassy, Jacros).
Daily Averaged PM2.5 and Black Carbon
3/2022-11/2022 | 3/2022-11/2022 | 8/2022-9/2022 | 11/2021-6/2022 | 3/2021-8/2022

## Slide 13
Surface PM Monitoring Sites in South Africa PTA
SAAQIS
SPARTAN
AMOD
PTA Bounding box

## Slide 14
Surface PM Monitoring Sites in South Africa PTA
Johannesburg
University of Johannesburg Kingsway Campus
Pretoria
Council for Scientific and Industrial Research
Thatchfield, Centurion
AirPhoton SS5 PM2.5 Sampler
(SPARTAN Network)
AMOD Sampler

## Slide 15
Preliminary Surface PM Monitoring Results in South Africa PTA
Data source: SAAQIS
Seasonal Average PM2.5 in South Africa PTA (2021)
PM2.5 levels are generally higher in fall and winter due to a combination of increased emissions from sources such as biomass burning and wind-blown dust, as well as more stagnant conditions.
PM2.5 shows a distinct spatial gradient, with the highest levels in the densely populated Gauteng Province (Cities of Ekurhuleni, Johannesburg, Sedibeng, Tshwane) and lowest levels in smaller cities in other provinces (e.g., Mpumalanga)

## Slide 16
Preliminary Surface PM Monitoring Results in South Africa PTA
Province
City
Site
Average Diurnal PM2.5 by Site and Season in South Africa PTA (2021)
Data source: SAAQIS
All sites and cities exhibit a clear PM2.5 diurnal trend, with peaks in the morning (8-9am) and at night (7-9pm).
The peaks are more pronounced during the winter and fall seasons.

## Slide 17
Preliminary Surface PM Monitoring Results in South Africa PTA
Seasonal Average PM2.5 Composition Measured by the SPARTAN Station in Pretoria (4/2021-2/2022)
Higher PM2.5 levels in fall and winter are also evident in the SPARTAN data.
Residual matter (representative of organic matter), black carbon, ammonium sulfate, and dust make up the majority of PM2.5 mass, respectively.
Ammonium nitrate accounts for only 2% of total PM2.5 mass.
Average black carbon concentrations range from 2 µg/m3 (~15% of total mass) in summer to 5.5 µg/m3 (~30% of total mass) in winter.

## Slide 18: Summary
The MAIA satellite instrument will be launched next year (flight mission duration: 3 years), in partnership with the Italian Space Agency.
MAIA will generate daily maps of total PM2.5, total PM10, and speciated PM2.5 (sulfate, nitrate, EC, OC, dust) at 1-km spatial resolution in 11 primary target areas (PTAs).
Two PTAs are in Africa: Ethiopia (Addis Ababa and vicinity) and South Africa (Johannesburg and vicinity).
MAIA surface PM monitor deployments in the African PTAs are near completion and data are starting to be acquired.
MAIA-EVI data products will be publicly available at NASA’s Atmospheric Science Data Center.
Epidemiologists on the MAIA-EVI Science Team will investigate linkages between PM type and human health.
maia.jpl.nasa.gov
Sina.Hasheminassab@jpl.nasa.gov

## Slide 19: Acknowledgments
The MAIA project is grateful to the field team members involved in the installation, operation, and maintenance of the air monitoring equipment, as well as those involved in laboratory analysis and data processing.
The US Agency for International Development (USAID) has provided funding to supplement MAIA's activities in Africa.
The US Department of State (USDOS) facilitates shipments of the air monitoring equipment and consumables. USDOS is also hosting some of the air monitoring equipment at the embassy sites.